## Slide 1: ECE 4180 Final Project: Balancing Buddy
Daniel Niemann, Fan Han Hoon, Sid Gulati, Muath F Alsubhi

## Slide 2: Project Introduction
Primary Objective:
  Construct a robot from already-owned parts that can autonomously maintain its balance in real time with zero help
Challenges Encountered:
  Sensitivity of selected IMU
    We went through 4 different IMUs before landing on our final choice
  Off-axis center of gravity
    Due to servo placement
  Issues with balancing calculation
    Wild distribution of results
    A library used for IMU was found to be flawed

## Slide 3: Hardware Overview
IMU of Choice: LSM9DS0
Use Mbed instead of Arduino or Pi Zero
  Lots of libraries that were already available + familiarity with the platform
IMU
LSM9DS0
AA Batteries
Mbed
LPC1768
H-Bridge
TB6612FNG
Right Motor
Left Motor
Balancing
Robot!
Angular Acceleration
Gyro Reading
Power (5V)
Power (5V)
Power (5V)
Speed (PWM)
Direction

## Slide 4
Driven by mbed code through H-bridge
Dual Servo Motors
Power Supply (5V)
4 AA batteries in parallel allow for long battery life
Mbed: LPC1768
Takes input from Mbed and scales servo power accordingly
H-Bridge: TB6612FNG
Runs balancing software, reads IMU and controls servos
IMU: LSM9DS0
Reads gyro and accelerometer data and sends to Mbed
Since the balancing point is in front of the chassis due to servo placement, all weight was placed on the front of the device to create a balancing point for the device that lets it stand straight up

## Slide 5: Software & Programming
Motor Code (Identify Motor Bias)
  Rev/s, Linear Speed, Time
  Heading Angle
  Bias
2 Mode
  Equilibrium Mode (Identify IMU Bias)
  Balancing Mode (PID Control)

## Slide 6: Demo

## Slide 7: Summary & Future Work
In the static balance test, the robot performed exceptionally
Robot encountered small hiccups with dynamic balance test
  Sometimes, servo would overcommit once the robot tilted past 50 degrees in either direction
Future Additions:
  Bluetooth module with virtual joystick to control device
  Lidar sensor to sense objects in robot’s path
  Speaker to play funny music